## Slide 1: Consume Local
Aravindh Raman‡, Dmytro Karamshuk‡, Nishanth Sastry‡,
Andrew Secker†, Jigna Chandaria†
‡ King’s College London, UK
† BBC R&D, London, UK
Towards Carbon-free Content Delivery
Notes: Buy Local– users like to buy local
– consume local – Netflix
Rethink buy local
example. Enabling Carbon free content delivery through peer-assisted content delivery
In collab. with BBC. BBC decrease the carbon-footprint
take through Peer-assisted content delivery

## Slide 2: Peer-assisted Content Delivery
Internet
Core Router
PoP
ExP
How many peers close-by?
Edge devices are energy-expensive
Notes: Traditional deliver => Server -> to the user
What peer-assistance enables
How close the user are and how popular the content is. Niche interest
Core-router would be few kw, ExP per user energy foot print – differential cost could be high
How traditional way could be better.
Each hop is expensive – per user cost is expensive

## Slide 3: Research Questions?
Does P2P content sharing save energy? – YES!!
  Model energy savings from P2P
  Evaluate the savings using real time data access
How can users be incentivized for sharing the content? – CCT!!
  Through Carbon Credit Transfers (CCT)
  CCT makes users carbon positive
Notes: Does P2P content save energy?
What’s the benefit to the users.
Carbon-Offset
Will start with modelling

## Slide 4: Modelling
p ( G * TU )
s ( (1 – G) * TU )
s ( TU )
Energy Savings (S) = 1 –
+
Energy consumed = Energy consumed by user traffic thru’ (traditional CDN + peer-assisted)
G => Fraction of traffic saved by P2P offload
s => per bit energy cost from servers
p => per bit energy cost for P2P
TU => User Traffic
Notes: We calculate the energy consumed per bit – fraction of traffic saved
Calculation of s is Straightforward.
G and talk about the capacity – the more the user the close-by you save the energy
Closed-form solution
We calculate the energy consumed per bit – fraction of traffic saved
Calculation of ψs is Straightforward.
G and talk about the capacity – the more the user the close-by you save the energy
Closed-form solution

## Slide 5: Energy Savings Formulation
X
S =
=> Upload bandwidth per user
=> bit rate of the video
=> Swarm size
Chart: 
Swarm Size ()
Energy Savings (S)
Notes: Savings can be calculated as a difference between total energy saving made by cdn and energy consumed by P2P
There are three important factors – q/B and c
General intuition of C, q/beta. The ratio matters.
P2p swarm saving is limited by amount you upload. More the upload more savings. Bit rates.
Larger the swarm size, shorter the hop.

## Slide 6: Dataset
3M users/month
23.5M sessions/month
1.5M IPs/month
Population: 8M

## Slide 7: Energy Calculations
 | Content Server (nJ/bit) | Core Router (nJ/bit) | PoP (nJ/bit) | ExP (nJ/bit) | End user (nJ/bit)
Baliga et al. [1] | 281.3 | 245.74 | 197.48 | 144.86 | 100.0
Valancius et al. [2] | 211.1 | 900.0 | 600.0 | 300.0 | 100.0
[1] J. Baliga, R. W. A. Ayre, K. Hinton and R. S. Tucker, "Green Cloud Computing: Balancing Energy in Processing, Storage, and Transport," in Proceedings of the IEEE, vol. 99, no. 1, pp. 149-167, Jan. 2011.
[2] V. Valancius, N. Laoutaris, L. Massoulié, C. Diot, and P. Rodriguez. Greening the internet with nano data centers. In Proceedings of the 5th international conference on Emerging networking experiments and technologies, pages 37–48. ACM, 2009.
Notes: While q and beta matters, there are other constants we need to take care of
Cited more than 500 times

## Slide 8: Swarm Size vs Energy Savings
Popular (100k views)
Semi-Popular (10k views)
Unpopular (1k views)
Theory matches practical savings
O ISP 1 O ISP 2 O ISP 3 O ISP 4 O ISP 5
Notes: How theoretical savings fit the practical savings

## Slide 9: Savings across the corpus
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
ISP 1 | 0.167 | 0.172 | 0.1989 | 0.1963 | 0.17896 | 0.1887 | 0.1769 | 0.1805 | 0.1796 | 0.1907 | 0.2005 | 0.1996 | 0.1895 | 0.1793 | 0.18018 | 0.18247 | 0.19667 | 0.1953 | 0.18323 | 0.18475 | 0.17879 | 0.17845 | 0.18121 | 0.19324 | 0.1978 | 0.19072 | 0.17998 | 0.17932 | 0.18467 | 0.18125
ISP 4 | 0.1205 | 0.1332 | 0.1575 | 0.1553 | 0.1393 | 0.1562 | 0.1389 | 0.1395 | 0.1434 | 0.1472 | 0.1613 | 0.1592 | 0.1589 | 0.13945 | 0.1382 | 0.1435 | 0.15805 | 0.14432 | 0.14326 | 0.15072 | 0.14972 | 0.14836 | 0.14124 | 0.15797 | 0.14131 | 0.14472 | 0.14368 | 0.14074 | 0.14113 | 0.14124
ISP 5 | 0.09932 | 0.11057 | 0.12266 | 0.1231 | 0.10979 | 0.12007 | 0.11672 | 0.11992 | 0.11958 | 0.11893 | 0.13143 | 0.12052 | 0.10856 | 0.10152 | 0.10079 | 0.11156 | 0.12132 | 0.11932 | 0.11056 | 0.11753 | 0.10673 | 0.10172 | 0.11378 | 0.12053 | 0.13197 | 0.11927 | 0.11826 | 0.11805 | 0.11923 | 0.11813
18% of average energy savings per day
Day
Energy Savings (S)

## Slide 10: Incentivizing Users at System level
Energy Savings (S)
Swarm capacity (c)
Chart: 
Notes: Two major players
CDN is doing nothing
User Uploading all time – why?
One part benefiting – one part suffering
Why we need to do this?
We see this as carbon credits.

## Slide 11: Carbon Credits
Notes: What are these carbon credits?
when you booked your flight ticket you might have noticed – offsetting carbon

## Slide 12: Carbon Credit Transfers

## Slide 13: So, Carbon Neutral?
80% the users become carbon positive

## Slide 14: Cache and Share?

## Slide 15: Cache and Share?
Internet
15
Core Router
PoP
ExP
Notes: Advantages of caching than p2p

## Slide 16: Feasible?
Luton (4993/sq.km)
Cambridge (3193/sq.km)
Milton Keynes (847/sq.km)
Boston (183/sq.km)
Eden (25/sq.km)
Hammersmith and Fulham (11213/sq.km)

## Slide 17: How to Share?
Wi-Stitch
Who Operates?
  MNOs and Fixed line ISP
  Content Providers
How do users access?
  WiFi
  mmWave
  Cellular network
How to locate content?
  ICN
  NFV/SDN
  HTTP/DNS redirection

## Slide 18: Store and Share (optimally)

## Slide 19
Go Green, in fact Carbon positive
Upto 30% of energy savings
[Best Paper] Aravindh Raman, Nishanth Sastry, Arjuna Sathiaseelan, Jigna Chandaria and Andrew Secker. Wi-Stitch: Content Delivery in Converged Edge Networks. In Proceedings of SIGCOMM MECOMM (2017)
Aravindh Raman, Dmytro Karamshuk, Nishanth Sastry, Andrew Secker and Jigna Chandaria. Consume Local: Towards Carbon Free Content Delivery In 38th IEEE ICDCS (2018).
Aravindh Raman, Nader Mokari, Mostafa Salehi, Tooba Faisal, Andrew Secker, and Jigna Chandaria Care to Share? An Empirical Analysis of Capacity Enhancement by Sharing at the Edge, Mobicom EdgeTech Workshop (2018) .

## Slide 20: [Dataset available] See https://bit.ly/wi-stitch
20
20

## Slide 21: [WIP (Please get in touch if interested!)]
When does sharing become feasible?
  Clearly works for BBC but won’t work for Parliamentlive.tv 
Rough model
  Users are picking content items from a bin (e.g., based on power law)
  Users then clump together into cells (e.g., some point process, which is inhomogenous to induce clumping into villages)
As a graph:
  Colour nodes based on content item
  Probabilistically induce edges based on closeness
  When does each colour of the graph become connected?

## Slide 22
Go Green, in fact Carbon positive
Upto 30% of energy savings
[Best Paper] Aravindh Raman, Nishanth Sastry, Arjuna Sathiaseelan, Jigna Chandaria and Andrew Secker. Wi-Stitch: Content Delivery in Converged Edge Networks. In Proceedings of SIGCOMM MECOMM (2017)
Aravindh Raman, Dmytro Karamshuk, Nishanth Sastry, Andrew Secker and Jigna Chandaria. Consume Local: Towards Carbon Free Content Delivery In 38th IEEE ICDCS (2018).
Aravindh Raman, Nader Mokari, Mostafa Salehi, Tooba Faisal, Andrew Secker, and Jigna Chandaria Care to Share? An Empirical Analysis of Capacity Enhancement by Sharing at the Edge, Mobicom EdgeTech Workshop (2018) .

## Slide 23: Back up slides

## Slide 24: Traffic Gain
swarm capacity can be modelled as M/M/∞
=> p = 1 − e−c
G =
= )
= (
G =

## Slide 25: Per-bit cost from servers
G
s
p
S
PUE => power usage efﬁciency metric of the network
ɭ => is the energy “loss” for end-user equipment.
s = + ɭ

## Slide 26: Per-Bit Energy Consumption for P2P trafﬁc
=
PoP
ExP

## Slide 28: Store and Share (WIP)
?

## Slide 29: Carbon Credits
Notes: Markets for carbon credits

## Slide 30: Per-bit cost for P2P
G
s
p
S
p = 2ɭ
(L) = ((L) )
+ ((L) − (L) )
+ ((L)− (L) )